## Slide 1: Experimental Design For Engineers
ISYE435-535

## Slide 2: Factors for Boiling Water
Boiling water:
  Factors: pan type, burner size, cover
  Response: time to boil water
Can you think of other
factors?

## Slide 3: What is Response Surface Analysis?
Definition
It is a combination of Regression plus Design of Experiments in order to “Optimize” a real System.

## Slide 4: RSM – Regression
We are going to fit a model similar to this:

## Slide 5: RSM – Optimization
Look for the setting (x1,x2) that produces the best value for y.
Setting of Tool angle (x1) and Speed (x2) that produces the best life (y).

## Slide 6: RSM – Design of Experiments
It has to do with how to collect data at a minimum cost to produce the necessary amount of information that allows us to fit a surface to optimize our system.

## Slide 7: Introduction to DOE
An experiment is a test or a series of tests
Experiments are used widely in the engineering world
  Process characterization & optimization
  Evaluation of material properties
  Product design & development
  Component & system tolerance determination
“All experiments are designed experiments, some are poorly designed, some are well-designed”

## Slide 8: Engineering Experiments
Reduce time to design/develop new products & processes
Improve performance of existing processes
Improve reliability and performance of products
Achieve product & process robustness
Evaluation of materials, design alternatives, setting component & system tolerances, etc.

## Slide 9: Four Eras in the History of DOE
The agricultural origins, 1918 – 1940s
  R. A. Fisher & his co-workers
  Profound impact on agricultural science
  Factorial designs, ANOVA
The first industrial era, 1951 – late 1970s
  Box & Wilson, response surfaces
  Applications in the chemical & process industries
The second industrial era, late 1970s – 1990
  Quality improvement initiatives in many companies
  Taguchi and robust parameter design, process robustness
The modern era, beginning circa 1990

## Slide 10
R. A. Fisher (1890 – 1962)
George E. P. Box

## Slide 11: The Basic Principles of DOE
Randomization
  Running the trials in an experiment in random order
  Notion of balancing out effects of “extraneous” variables
Replication
  Sample size (improving precision of effect estimation, estimation of error or background noise)
  Replication versus repeat measurements?
Blocking
  Dealing with nuisance factors

## Slide 12: Strategy of Experimentation
“Best-guess” experiments
  Used a lot
  More successful than you might suspect, but there are disadvantages…
One-factor-at-a-time (OFAT) experiments
  Sometimes associated with the “scientific” or “engineering” method
  Devastated by interaction, also very inefficient
Statistically designed experiments
  Based on Fisher’s factorial concept

## Slide 13: Factorial Designs
In a factorial experiment, all possible combinations of factor levels are tested
The golf experiment:
  Type of driver (Oversized or Regular)
  Type of ball (Balata or Three-piece)
  Walking vs. riding
  Type of beverage (Water or Beer)
  Time of round
  Weather
  Type of golf spike
  Etc, etc, etc…

## Slide 14: Factorial Design

## Slide 15: Factorial Designs with Several Factors

## Slide 16: Factorial Designs with Several Factors A Fractional Factorial

## Slide 17: Planning, Conducting & Analyzing an Experiment
Recognition of & statement of problem
Choice of factors, levels, and ranges
Selection of the response variable(s)
Choice of design
Conducting the experiment
Statistical analysis
Drawing conclusions, recommendations

## Slide 18: Planning, Conducting & Analyzing an Experiment
Get statistical thinking involved early
Your non-statistical knowledge is crucial to success
Pre-experimental planning (steps 1-3) vital
Think and experiment (use the KISS principle)

## Slide 19: Planning, Conducting & Analyzing an Experiment
Cause-effect diagram

## Slide 20: Think of Factors
Microwave popcorns:
Factors:
Response: taste
Photography:
Factors:
Response: quality of slides

## Slide 21: Propose your own examples
Give two examples:

## Slide 22: DOE/RSM – Optimization
Screening
Improvement
Optimization